## Slide 1
By
Name : N.P.K.D.Wickramasekara
Index No : 15398
Course : PH 3032 - Embedded Systems Laboratory
WEARABLE COMPUTER MOUSE

## Slide 2
CONTENTS
  Introduction
  Solution
  How does this work?
  Functionalities
  Functionalities of the ATmega32
  Hardware and Microcontroller
  Circuit diagram
  Process
  Main Pr﻿oblems

## Slide 3
INTRODUCTION
In the world of modern computing, the need for more intuitive and portable computer input devices has become increasingly pronounced. The traditional computer mouse, while a stalwart tool for navigating digital landscapes, comes with inherent limitations that impact the user experience.
Problems
  Using one hand for mouse?
  Can a person who can only use their fingers operate the mouse?
  Do we need a table for using this mouse?

## Slide 4
  Wearable Mouse
SOLUTIONS
We can use the mouse by moving only one finger and perform right-click and left-click actions with a single finger. By moving two fingers, we can control the mouse. We do not need a table to use the mouse. With this wearable mouse project, we can control the mouse without moving the entire hand.

## Slide 5
HOW DOES THIS WORK?
GET DATA
Ring
Microcontroller
Computer
SEND DATA

## Slide 6
HOW DOES THIS WORK?
MEASUREMENTS
X
Y

## Slide 7
X
HOW DOES THIS WORK?
WORKING WITH A COMPUTER SCREEN
Y
X
Y

## Slide 8
X
HOW DOES THIS WORK?
WHAT CAN WE USE TO TAKE MEASUREMENTS?
Y

## Slide 9
FUNCTIONALITIES
    Getting x and y-axis data for cursor movement.
    Functionality of the start button.
    Functionality of the left-click button.
    Functionality of the right-click button.

## Slide 10
    Getting x and y-axis data for cursor movement.
FUNCTIONALITIES
Ring

## Slide 11
Start
Right Click
Left Click
FUNCTIONALITIES
    Functionality of the start button.
    Functionality of the left-click button.
    Functionality of the right-click button.

## Slide 12
FUNCTIONALITIES OF THE ATMEGA32
1. ADC (Analog-to-Digital Converter):
ADC allows the microcontroller to convert analog signals (e.g., sensor data) into digital values for processing.

## Slide 13
FUNCTIONALITIES OF THE ATMEGA32
2. Serial Communication:
  Serial communication enables data exchange between the microcontroller and external devices, such as your computer. It's crucial for transmitting and receiving data.

## Slide 14
FUNCTIONALITIES OF THE ATMEGA32
3. Interrupts:
  Interrupts are used for handling time-sensitive events. They allow the microcontroller to respond quickly to specific triggers, like button presses or sensor data changes.

## Slide 15
HARDWARE AND MICROCONTROLLER

## Slide 16
ATMEGA32 MICROCONTROLLER
We selected the ATmega32 microcontroller for our project for several reasons. It is a cost-effective option, consumes minimal energy, and is user-friendly for uploading and executing code.
PUSH BUTTON
In addition to the microcontroller, our wearable device incorporates several key components. Push buttons play a crucial role, serving as interrupt triggers for functions such as left-click, right-click, and initiating cursor movement.
UART SERIAL ADAPTOR MODULE
  To facilitate communication between the computer and the microcontroller, we implemented UART (Universal Asynchronous Receiver-Transmitter). This choice not only offered seamless data transfer but also kept the design compact and budget-friendly.
IR LED AND PHOTO DIODE
  To enable distance measurement, we integrated an IR (Infrared) LED and a photodiode into our design. These components were not only budget-friendly but also allowed for easy placement, given their compatibility with the design's non-circuit module structure. This setup effectively supports the device's functionality.

## Slide 17
CIRCUIT DIAGRAM

## Slide 18
CIRCUIT DIAGRAM

## Slide 19
PROCESS
  The ATmega32 microcontroller is responsible for reading data from the photodiode. It utilizes the Analog-to-Digital Converter (ADC) to convert incoming analog voltage values into digital data that can be processed.
01

## Slide 20
PROCESS
  The captured data is then processed within the microcontroller. Once processed, the information is ready for transmission to a computer.
  To achieve this communication, the ATmega32's TX (Transmit) pin is connected to the UART's RX (Receive) pin, enabling data to flow from the microcontroller to the computer.
  Additionally, the ATmega32's RX (Receive) pin is connected to the UART's TX (Transmit) pin, ensuring a two-way data exchange.
02

## Slide 21
PROCESS
  In Python, we can seamlessly interface with our wearable device to capture serial data and translate it into real-time cursor movement.
  To achieve this, we employ three essential modules:
  Serial Module
  PyAutoGUI Module
  Time Module
03

## Slide 22
PROCESS
  By harnessing the power of these Python modules, we bridge the gap between the data collected by the wearable device and the seamless cursor control on your computer screen. The result is a fluid and user-friendly experience that transforms finger movements into intuitive cursor navigation.
03

## Slide 23
MAIN PROBLEMS
1. FINDING THE PERFECT SENSOR
2. DEALING WITH LONG WIRE CONNECTIONS
3.INTEGRATING COMPONENTS INTO THE RING

## Slide 24
THANK YOU!